## Slide 1: BS Data Science 2nd Semester Lecture
Presented By
Dr. Arifa Mirza
Punjab University College of Information Technology
Applied Physics
Electromagnetic Induction

## Slide 2
Faraday’s Law of Electromagnetic Induction

## Slide 3
A primary coil is connected to a switch and a battery.
The wire is wrapped around an iron ring.
A secondary coil is also wrapped around the iron ring.
There is no battery present in the secondary coil.
The secondary coil is not directly connected to the primary coil.
Faraday’s Experiment – Set Up

## Slide 4: Electromagnetic Induction

## Slide 5: Faraday’s Law of Induction
A changing magnetic flux induces an EMF

## Slide 6: Magnetic Flux Thru Wire Loop
Analogous to Electric Flux (Gauss’ Law)
(1) Uniform B
(2) Non-Uniform B

## Slide 7: What is EMF?
Looks like potential. It’s a “driving force” for current

## Slide 8: Faraday’s Law of Induction
A changing magnetic flux induces an EMF, a curling E field

## Slide 9: Minus Sign? Lenz’s Law
Induced EMF is in direction that opposes the change in flux that caused it

## Slide 11
Faraday’s law indicates that the induced emf and the change in flux have opposite algebraic signs.
This has a physical interpretation that has come to be known as Lenz’s law.
Developed by German physicist Heinrich Lenz
Lenz’s law: the induced current in a loop is in the direction that creates a magnetic field that opposes the change in magnetic flux through the area enclosed by the loop.
The induced current tends to keep the original magnetic flux through the circuit from changing.

## Slide 13: Faraday’s Law of Induction
Changing magnetic flux induces an EMF
Lenz: Induction opposes change

## Slide 14: Ways to Induce EMF
Quantities which can vary with time:
Magnitude of B
Area A enclosed by the loop
Angle q between B and loop normal

## Slide 15: Group Problem: Changing Area
Conducting rod pulled along two conducting rails in a uniform magnetic field B at constant velocity v
Direction of induced current?

## Slide 16: Faraday’s Experiment – Findings
At the instant the switch is closed, the ammeter changes from zero in one direction and then returns to zero.
When the switch is opened, the ammeter changes in the opposite direction and then returns to zero.
The ammeter reads zero when there is a steady current or when there is no current in the primary circuit.

## Slide 17
Faraday’s Experiment – Conclusions
An electric current can be induced in a loop by a changing magnetic field.
  This would be the current in the secondary circuit of this experimental set-up.
The induced current exists only while the magnetic field through the loop is changing.
This is generally expressed as: an induced emf is produced in the loop by the changing magnetic field.
  The actual existence of the magnetic flux is not sufficient to produce the induced emf, the flux must be changing.

## Slide 18
Faraday’s Law of Induction Statements
The emf induced in a circuit is directly proportional to the time rate of change of the magnetic flux through the circuit.
Remember FB is the magnetic flux through the circuit and is found by
If the circuit consists of N loops, all of the same area, and if FB is the flux through one loop, an emf is induced in every loop and Faraday’s law becomes